| TIN No. : 07-21 | Revision No. : 1 | Issue Date : 16 7 21 |
| --- | --- | --- |
| Title : Sherwood Ranger Main Wheel Hub |
| Applicability: |
| Information Type(s) Sherwood Ranger ST and XP |
| Modification |  | Airworthiness / MPD | X | Maint / Operation |  |
| Parts |  | Inspection |  | Other |  |
| Importance: ESSENTIAL / HIGH / ROUTINE |
| Subject Summary / Description of Problem: It has been found on Sherwood Rangers of in excess of 200 hours, or those with high landing cycles, those that have long taxi journeys or those that have had hard landings that the outer retaining ring of the outer wheel bearing in the wheel hub can break off. The failure of the retaining ring can in certain circumstances allow the bearing spacer ring to seize on the inner bore of the wheel hub, which on the right-hand wheel can lead to the wheel nut tightening and potentially cause the wheel to lock up. |
| Parts / Assemblies Affected: 7-UA30 wheel hub, 7-UC4 Wheel bearing and UA30 Bearing Pre Load Spacer |
| Action Required: Inspection and replacement of the hub with replacement of bearings and preload spacer if necessary |
| Authorised on Behalf of TLAC : Paul Hendry-Smith Director Position : Signature : |