Technical Bulletin: Sherwood Ranger Main Landing Wheel Hub

An issue has become apparent that the wheel hub flange may crack as per image below.

Fig 1.

Resolution: -

Replacement Of Wheel hub assembly with part number :7-UA30

Process: -

Safely jack and support the main landing wheel

Remove hub nut 11/16” and remove wheel complete with brake drum

Fig 2

Remove Brake Drum 3 x 4mm Socket head screws

Fig 3

Remove 6 wheel nuts to remove hub unit

Warning: Split Rim wheel let pressure out of tyre before removing wheel nuts

Fig 4

Fig 5.

Remove 6 x wheel bolts from Hub

.Press out Wheel Bearings from Hub (Only necessary on bare hub units)

Reassemble Bearings, bearing spacer and wheel bolts onto new hub

Fig 6

On inner rim of Wheel carefully Radius the inner bore

Ensure the Hub sits flat on the inner rim

Re assemble wheel Brake Drum and refit wheel to aircraft